## Slide 1: CusToM Workshop - Kinematic tutorial
Charles Pontonnier, Pierre Puchaud

## Slide 2: Generate Parameters of the Model
  Size : 1.755 m
  Mass : 70 Kg
Osteo-articular model – full body
  Pelvis
  Pelvis LowerTrunk
  Leg
  Arms
Marker Set
  MarkerSet_2 (M2S makerset)
  2 markers on hand
No Muscles

## Slide 3: AnalysisParameters
Only Inverse Kinematic Active Step
  Levenberg-marquardt
  5Hz filter butterworh 2nd order zero lag

## Slide 4: What CusToM is Doing ?
The osteoarticular model comes from cadaveric data.
Anthropometric scaling:
  Segments lengths
  Anatomical landmarks

## Slide 5: What CusToM is Doing ?
A priori known location of anatomical landmarks are computed in the global reference frame function of joint coordinates
Jacobian matrix are computed analytically
  For Inverse kinematics using Levenberg-Marquardt algorithms

## Slide 6: What CusToM is Doing ?
Euclidian distance minization between experimental markers and a priori know location of anatomical landmarks in the global frame
We get the joint coordinates .

## Slide 7: First results – Kinematic residuals

## Slide 8: First results – Joint coordinates

## Slide 9: What about the quality of the model ? – Right Shank length

## Slide 10: What about the quality of the model ?
For a same size, segment lengths can vary between subjects.

## Slide 11: Enhancing the Osteoarticular model
We will add a geometric calibration step
Folder : SideStep_Geometric_Calibration
Same previous steps, except for AnalysisParameters.

## Slide 12: Geometrical Calibration step
Frames used
  Selection method of frames : UniformlyDistributed
  Number of frames : 20
Body length
  Homethetic factors of Clavicles are linked to homothetic factor of the Thorax
Marker Position
  Direction of markers to optimize in local frames ( Z is medio-lateral )
Axis of rotation
  Orientation of Joint axis can be optimized to fit subject-specific joint axis.
  For example knee axis. Two rotation angles have to be introduced.

## Slide 13: What is CusToM Doing ?
A priori known location of anatomical landmarks are computed in the global reference frame ,function of:
joint coordinates ,
homothetic factors ,
variation of marker position ,
rotation of joint axis .

## Slide 14: What is CusToM Doing ?
Uniformely distributed frames
Frames are chosen equally spaced in ROM.c3d

## Slide 15: What is CusToM Doing ?
Body Length
Linear Constraints of homothetic factors.

## Slide 16: What is CusToM Doing ?
Axis of rotation
Some location of markers are optimized
In this case :
RKNE is trusted for x,y,z direction
RKNI is trusted for x direction and optimized for y and z direction
RKNE
RKNI

## Slide 17: What is CusToM Doing ?
Axis of rotation

## Slide 18: What is CusToM Doing ? – Geometrical Calibration Process
Regression method
Based on height
RM
Equally spaced sets of frames:
Parameters identification
At each iteration i
  Muller et al. 2015
Lu and O’Connor et al. 1999
Criterion satisfied ?
Inverse kinematics

## Slide 19: What is CusToM Doing ?

## Slide 20: Calibration Results