## Slide 1: CusToM Workshop
Kinematic tutorial

## Slide 2: Generate Parameters of the Model
  Size : 1.755 m
  Mass : 70 Kg
Osteo-articular model – full body
  Pelvis
  Pelvis LowerTrunk
  Leg
  Arms
Marker Set
  MarkerSet_2 (M2S makerset)
  2 markers on hand
No Muscles

## Slide 3: AnalysisParameters
Only Inverse Kinematic Active Step
  Levenberg-marquardt
  5Hz filter butterworh 2nd order zero lag

## Slide 4: What CusToM is Doing ?
The osteoarticular model comes from cadaveric data.
Anthropometric scaling:
  Segments lengths
  Anatomical landmarks

## Slide 5: What CusToM is Doing ?
A priori known location of anatomical landmarks are computed in the global reference frame function of joint coordinates
Jacobian matrix are computed analytically
  For Inverse kinematics using Levenberg-Marquardt algorithms

## Slide 6: What CusToM is Doing ?
Euclidian distance minization between experimental markers and a priori know location of anatomical landmarks in the global frame
W.