## Slide 1: CusToM Workshop
Muscle forces tutorial
Charles Pontonnier, Pierre Puchaud

## Slide 2: Pre-work
1. Create a new folder in Examples and name it 2_SideStep_Muscle
2. Copy/paste SideStep_Geometric_Calibration folder in 2_SideStep_Muscle and rename it SideStep_Muscle_Opti
. Supress the BiomechanicalModel.mat file inside the folder SideStep_Muscle_Opti
Should look like this:
Examples folder

## Slide 3: Generate Parameters of the Model
First load parameters: size, mass, osteoarticular and marker sets are ok !
Add muscles to right and left legs
Classical Leg model [Daamsgard2006]
Generate Parameters

## Slide 4: Generate analysisParameters
First load parameters: kinematics are ok!
Open Inverse Dynamics options: enable
Select « From Experiments » for External forces
Open Options, select « DataInC3D »
Select « Lfoot » for Platform 1 and « Rfoot » for Platform 2
This is the source where external forces applied to the model will be read
This is a priori knowledge that you should know from your own experiments !!!!!

## Slide 5: Generate analysisParameters
First load parameters: kinematics are ok!
Open « Inverse Dynamics » options: enable
Select « From Experiments above » for External forces
Open Options, select « DataInC3D »
Select « Lfoot » for Platform 1 and « Rfoot » for Platform 2
Open « Muscle forces estimation » Options
Select Optimization problem, and Polynomial function (order 2)

## Slide 6: What does this mean ?
The resulting problem to solve for MS forces estimation will be:
s.t.

## Slide 7: Alternatives
Change order to
Change Polynomial Function to MinMax
Muscle synergy
Maximal Synergy
See
Rasmussen, J., Damsgaard, M., & Voigt, M. (2001). Muscle recruitment by the min/max criterion—a comparative numerical study. Journal of biomechanics, 34(3), 409-415.

## Slide 8: RUN

## Slide 9: What CusToM is doing ?
Not new
New
Analytical solution computed and gathered as a matlab function

## Slide 10: What CusToM is doing ?
Not new
Newton-Euler Algorithm

## Slide 11: Newton Euler-Algorithm
For more details, see 5_INVERSE-DYNAMICS.pdf
Charles Pontonnier, Pierre Puchaud

## Slide 12: Main issue
Equations of motion
External forces
()
Joint torques
(
Angles, angular velocities and accelerations
At time

## Slide 13: Newton Euler equations for a solid
external forces
solid mass
center of mass of the solid in (world) frame
angular velocity of the solid in
inertia matrix of the solid in
torque associated to external forces, expressed in at the center of mass
At center of mass
Acceleration momentum
(1)
(2)

## Slide 14: Spatial equations of motion [Featherstone2007]
Velocity of in :
Acceleration of in :
The center of mass acceleration becomes:
Replacing in (1), it comes

## Slide 15: Spatial equations of motion [Featherstone2007]
External forces torque expressed at
With
And
Finally:

## Slide 16: Spatial equations of motion [Featherstone2007]
That can be expressed with a matrix expression
!
(application produit vectoriel)
This compact expression involves two fundamental spatial algebra features for rigid body dynamics that are: spatial inertia matrix and spatial acceleration of

## Slide 17: Spatial inertia and spatial acceleration
Spatial inertia matrix: 6 x 6 Symmetrical matrix:
identity matrix
Spatial acceleration: not a physical acceleration

## Slide 18: Equations of motion of one solid in a polyarticulated chain of solids
…
solid at time (mass inertia )
(
(
(
polyarticulated solids with joints
(
(
(

## Slide 19: Newton-Euler algorithm
Recursive Newton-Euler algorithm
Knowing joint angles, joint velocities and joint accelerations at time
Computing cartesian and angular velocities of all bodies from the base to extremities
Computing joint reaction forces of all solids from extremities to the base
À un instant
For to do
End
For to do
,
End

## Slide 20: Newton-Euler algorithm
Solid position and orientation update
Joint axis between and orientation update
Spatial velocity update
Spatial acceleration update
!
Spatial  all is computed in
For to do
End
For to do
,
End

## Slide 21: Newton-Euler algorithm
Spatial acceleration quantities computation for solid
Joint reaction forces between solid and solid computation
Spatial inertia matrix computation for solid
Center of mass position update for solid
solid at time (mass inertia )
(
(
(
(
(
(
(Joint torque extraction )
For to do
End
For to do
,
End

## Slide 22: Summary
With synthetic notations:
4 steps Newton-Euler algorithm
(spatial velocity update)
(spatial acceleration update)
(computing actions of on )
(extracting joint torques)
!
This implementation ask for a knowledge of all quantities at point
Pour from to
Pour from to